## Slide 1: Hashed Alpha Testing
Chris Wyman
Morgan McGuire
Symposium on Interactive 3D Graphics and Games; February 25, 2017
Traditional
Hashed

## Slide 2: STory
Never, in my life, expected to write a paper about alpha testing

## Slide 3: STory
Never, in my life, expected to write a paper about alpha testing
15 months ago, I didn’t even know a problem existed with alpha test
Was sent a link to blog post on Computing Alpha Mipmaps
  Thought: “Really!? Alpha maps disappear with distance? Weird.”
  Forgot about the issue

## Slide 4: STory
Never, in my life, expected to write a paper about alpha testing
15 months ago, I didn’t even know a problem existed with alpha test
Was sent a link to blog post on Computing Alpha Mipmaps
  Thought: “Really!? Alpha maps disappear with distance? Weird.”
  Forgot about the issue
Recently: Talking about a different problem
  Had a bit of a miscommunication, ended up discussing this problem
  As part of the discussion, Morgan asked, “why don’t people just hash?”

## Slide 5: Moral:
Game developers: Share your problems; don’t assume we know them!
  Informal poll of a couple (former) academics: 0% knew about this problem

## Slide 6: Moral:
Game developers: Share your problems; don’t assume we know them!
  Informal poll of a couple (former) academics: 0% knew about this problem
Researchers: Don’t assume simple problems are solved

## Slide 7: Moral:
Game developers: Share your problems; don’t assume we know them!
  Informal poll of a couple (former) academics: 0% knew about this problem
Researchers: Don’t assume simple problems are solved
Students: Search for problems where you can have an impact
  Research need not be hard
  Hare-brained idea to accepted research paper: 12 weeks

## Slide 8: Why Do People Alpha Test?
Has advantages over alpha blend
  Order independent; cheap; forward or deferred
  Extends to MSAA via alpha-to-coverage

## Slide 9: But… Problem
Has advantages over alpha blend
  Order independent; cheap; forward or deferred
  Extends to MSAA via alpha-to-coverage
Alpha-tested geom can disappear w / distance

## Slide 10: But… Problem
Has advantages over alpha blend
  Order independent; cheap; forward or deferred
  Extends to MSAA via alpha-to-coverage
Alpha-tested geom can disappear w / distance
  Why? Cannot prefilter binary visibility queries

## Slide 11: So: Hashed Alpha Test
Use stochastic sampling to avoid the problem

## Slide 12: So: Hashed Alpha Test
Use stochastic sampling to avoid the problem
  Basic idea is replace standard test:
  With stochastic test:

## Slide 13: So: Hashed Alpha Test
Use stochastic sampling to avoid the problem
  Basic idea is replace standard test:
  With stochastic test:
  But, this flickers like crazy
  Want temporal stability, esp. under slight motion
  Use stable, procedural noise:

## Slide 14: What Does this Look Like?
Alpha Test
Hashed Alpha
Ground Truth

## Slide 15: Talk Takeaways
Stochasm addresses problems with alpha testing
  Converges to ground truth (OIT) with enough random samples

## Slide 16: Talk Takeaways
Stochasm addresses problems with alpha testing
  Converges to ground truth (OIT) with enough random samples
Hashing can give noise stable over time

## Slide 17: Talk Takeaways
Stochasm addresses problems with alpha testing
  Converges to ground truth (OIT) with enough random samples
Hashing can give noise stable over time
By constraining hash inputs:
  Control noise behavior
  Ensure samples remain largely stable between frames

## Slide 18: Talk Takeaways
Stochasm addresses problems with alpha testing
  Converges to ground truth (OIT) with enough random samples
Hashing can give noise stable over time
By constraining hash inputs:
  Control noise behavior
  Ensure samples remain largely stable between frames
Also applies to alpha-to-coverage, screen-door transparency, etc.

## Slide 19: Stochastic Sampling Works
Alpha test
1 sample
4 samples
16 samples
64 samples
OIT with
alpha blend

## Slide 20: Stochastic Sampling Works
Alpha test
1 sample
4 samples
16 samples
64 samples
OIT with
alpha blend
1 sample, selected uniformly
on interval [0..1]
N samples, selected uniformly
on interval [0..1]
Stochastic Alpha (aka stochastic transparency)
N samples, selected randomly
on interval [0..1]
Traditional Alpha
Alpha-to-Coverage
1/2
1/8
3/8
5/8
7/8

## Slide 21: Stochastic Sampling Works
Alpha test
1 sample
4 samples
16 samples
64 samples
OIT with
alpha blend
1 sample, selected uniformly
on interval [0..1]
N samples, selected uniformly
on interval [0..1]
Stochastic Alpha (aka stochastic transparency)
N samples, selected randomly
on interval [0..1]
Traditional Alpha
Alpha-to-Coverage
But stochastic algorithms change each frame, causing severe temporal flickering!
1/2
1/8
3/8
5/8
7/8

## Slide 22: Why Hashing?
Hashing long known as a way of ‘randomizing’
  See “Numerical Recipes” for an example PRNG using DES encryption

## Slide 23: Why Hashing?
Hashing long known as a way of ‘randomizing’
  See “Numerical Recipes” for an example PRNG using DES encryption
Good hash function properties:
  Determinism given fixed input i.e., gives the same value each frame
  Defined range of outputs e.g., in range [0…1)
  Uniformity over output range e.g., uniform outputs in range [0…1)

## Slide 24: Why Hashing?
Hashing long known as a way of ‘randomizing’
  See “Numerical Recipes” for an example PRNG using DES encryption
Good hash function properties:
  Determinism given fixed input i.e., gives the same value each frame
  Defined range of outputs e.g., in range [0…1)
  Uniformity over output range e.g., uniform outputs in range [0…1)
Can select hash so these have equivalent quality, modulo stability:
  if ( color.a < hash( fragPos ) ) discard; if ( color.a < drand48() ) discard;

## Slide 25: What Do I Mean BY “Stability”?
Diff image under motion,
uncorrelated samples
Unstable
Stable
Frame-to-frame diff
Frame-to-frame diff

## Slide 26: Achieving Hash Stability
Key: Discretize hash inputs in appropriate coordinate frame
  For small Δ:
  hash( floor( myPosition ) ) = hash( floor( myPosition + Δ ) )
  Tweaking this, allows us to control the scale of the stable noise, e.g.:
  hash( floor( myPosition / scale ) * scale )

## Slide 27: Achieving Hash Stability
Key: Discretize hash inputs in appropriate coordinate frame
  For small Δ:
  hash( floor( myPosition ) ) = hash( floor( myPosition + Δ ) )
  Tweaking this, allows us to control the scale of the stable noise, e.g.:
  hash( floor( myPosition / scale ) * scale )
Ideally, same geometry should yield same hash under:
  Camera translation or rotation
  Object translation or rotation
  Ideally, object skinning and deformation

## Slide 28: Choice of Coordinate Frame
.’s work for deformation (and skinning) assuming hashing of pre-deformed coordinates
* = being somewhat generous

## Slide 29: Choice of Coordinate Frame
.’s work for deformation (and skinning) assuming hashing of pre-deformed coordinates
* = being somewhat generous
Clear choices:

## Slide 30: Choice of Coordinate Frame
.’s work for deformation (and skinning) assuming hashing of pre-deformed coordinates
* = being somewhat generous
We selected object coordinates; can discuss why, offline

## Slide 31: Hashed Alpha Code

## Slide 32: Hashed Alpha Code
Compute ideal scale to get 1-pixel sized noise

## Slide 33: Hashed Alpha Code
Compute ideal scale to get 1-pixel sized noise
Use 2 scales, one smaller & one larger than
desired scale; akin to mipmapping

## Slide 34: Hashed Alpha Code
Compute ideal scale to get 1-pixel sized noise
Compute hashed noise samples at 2 discrete scales
Use 2 scales, one smaller & one larger than
desired scale; akin to mipmapping

## Slide 35: Hashed Alpha Code
Compute ideal scale to get 1-pixel sized noise
Compute hashed noise samples at 2 discrete scales
Linearly interpolate between noise scales
Use 2 scales, one smaller & one larger than
desired scale; akin to mipmapping

## Slide 36: Hashed Alpha Code
Compute ideal scale to get 1-pixel sized noise
Compute hashed noise samples at 2 discrete scales
Linearly interpolate between noise scales
Interpolating between two uniform distributions
does not give a new uniform distribution
This math corrects for this non-uniformity
Use 2 scales, one smaller & one larger than
desired scale; akin to mipmapping

## Slide 37: Hashed Alpha Code
Compute ideal scale to get 1-pixel sized noise
Compute hashed noise samples at 2 discrete scales
Linearly interpolate between noise scales
Clamp; alpha threshold of 0 makes no sense
Interpolating between two uniform distributions
does not give a new uniform distribution
This math corrects for this non-uniformity
Use 2 scales, one smaller & one larger than
desired scale; akin to mipmapping

## Slide 38: Hashed Alpha Code
Specific hash not important, if uniform and
takes R3 → [0…1)
We use:

## Slide 39: Hashed Alpha Code
User parameter to control size of noise:
1.0 = roughly pixel sized noise
2.0 = roughly 2x2 pixel sized noise
3.0 = roughly 3x3 pixel sized noise

## Slide 40: Some Results
Alpha test αt = 0.5
Hashed alpha test
Ground truth OIT
0.06 ms @ 10242
0.08 ms @ 10242
1.3 ms @ 10242
Performances not optimized; only demonstrative of relative costs

## Slide 41: Some Results
Adjust alpha [Castaño 2010]
Hashed alpha test
Ground truth OIT
0.06 ms @ 10242
0.08 ms @ 10242
1.3 ms @ 10242
Performances not optimized; only demonstrative of relative costs

## Slide 42: But Not Just Alpha!

## Slide 43: HASHED Sampling HAS OTHER USES
NEW! Not discussed in I3D paper: stable hashed sampling in other domains

## Slide 44: HASHED Sampling HAS OTHER USES
Shows there’s a problem with anisotropic hashing!
NEW! Not discussed in I3D paper: stable hashed sampling in other domains

## Slide 45: HASHED Sampling HAS OTHER USES
Can be addressed, mostly, by updating hash inputs
NEW! Not discussed in I3D paper: stable hashed sampling in other domains

## Slide 46
Hashing At Grazing Angles
Alpha test
Hashed alpha
Anisotropic
hashed alpha

## Slide 47: Results
Alpha test αt = 0.5
Hashed alpha test
Ground truth OIT

## Slide 48: Results
Alpha test αt = 0.5
Hashed alpha test
Ground truth OIT
Might ask:
Do I want noise nearby?
(Alpha test is OK here)

## Slide 49: Results
Hashed alpha test
(Faded in with LOD)
Ground truth OIT
Adjust alpha [Castaño 2010]

## Slide 50: Results
Hashed alpha test
(Faded in with LOD)
Ground truth OIT
Per-LOD threshold adjust
(Manual, “artist” driven)

## Slide 51: Helps WITH MSAA And A2C
Ground truth OIT
8x alpha-to-coverage
8x hashed alpha-to-
coverage

## Slide 52: Temporal Antialiasing
Alpha Hashed Alpha Ground Truth
Alpha Hashed Alpha Ground Truth
With Temporal Antialiasing
No Temporal Antialiasing

## Slide 53: Temporal Antialiasing
Might think, “based on stochastic sampling; of course TAA works well!”
  But hashed alpha designed for stability under tiny camera motions, e.g. TAA jitter

## Slide 54: Temporal Antialiasing
Might think, “based on stochastic sampling; of course TAA works well!”
  But hashed alpha designed for stability under tiny camera motions, e.g. TAA jitter
A couple approaches:
  Reduce global noise scale to < 1 pixel
    TAA integrates sub pixel noise samples
  Jitter offset in hash space;
    Hash on objPos+offset[i] rather than objPos for relatively large, uncorrelated offset[i]
  Jitter the alpha threshold
    Compute αT = hash( objPos ), use thresholds fract( αT + i/N ) for i in [0…N)

## Slide 55: Summary
Introduce new approach for alpha testing:
  Alpha threshold cheaply & procedurally selected via a hash function
  Gives stable noise; roughly as stable as traditional alpha test

## Slide 56: Summary
Introduce new approach for alpha testing:
  Alpha threshold cheaply & procedurally selected via a hash function
  Gives stable noise; roughly as stable as traditional alpha test
Still use one alpha test per pixel, allowing:
  Use in both deferred and forward pipelines
  Run on older hardware; no new (or recent) features required

## Slide 57: Summary
Introduce new approach for alpha testing:
  Alpha threshold cheaply & procedurally selected via a hash function
  Gives stable noise; roughly as stable as traditional alpha test
Still use one alpha test per pixel, allowing:
  Use in both deferred and forward pipelines
  Run on older hardware; no new (or recent) features required
Requires nothing in asset pipeline
  Directly uses mip-chain’s alpha channels representing pre-filtered visibility

## Slide 58: Summary
Introduce new approach for alpha testing:
  Alpha threshold cheaply & procedurally selected via a hash function
  Gives stable noise; roughly as stable as traditional alpha test
Still use one alpha test per pixel, allowing:
  Use in both deferred and forward pipelines
  Run on older hardware; no new (or recent) features required
Requires nothing in asset pipeline
  Directly uses mip-chain’s alpha channels representing pre-filtered visibility
Can apply in other domains where stable shading locations important

## Slide 59: Questions?
Alpha Test
Hashed Alpha
Ground Truth
cwyman@nvidia.com
@_cwyman_